## Slide 1
QUISITIVE | SECURE INFRASTRUCTURE
Silent Packet Death in
Azure VMware Solution
Routing limits, hidden ceilings, and the design decisions that keep a migration from failing on Monday morning.
Enterprise network architects · Cloud engineers · Infrastructure directors
Notes: Framing: AVS networking failures are rarely loud. They show up as timeouts and retransmissions long after a migration is declared successful. This session works through where those limits live and how to design around them.

## Slide 2
THE SCENARIO
A successful migration that failed on Monday
FRIDAY
Preparation complete
Roughly 1,000 virtual machines staged for a weekend move into Azure.
SATURDAY
Cutover executed
The migration team runs the cutover on schedule with no reported errors.
SUNDAY
Connectivity verified
Application connectivity is tested and the migration is declared successful.
MONDAY
Hybrid connectivity fails
Production demand rises and the hybrid environment loses connectivity.
Monitoring told the team nothing
No obvious warnings · No useful error codes · No indication that routing capacity had been exceeded
Notes: The point of the scenario: every checkpoint passed. The limit that was breached is not exposed by ordinary monitoring, so the failure surfaces only under production load.

## Slide 3
THE CENTRAL PROBLEM
What silent packet death looks like
The environment reaches a mathematical limit inside the software-defined networking fabric. Nothing reports it directly.
Packets disappear
Traffic is dropped inside the switching or forwarding layer with no notification.
Applications time out
Sessions stall and retransmit rather than failing cleanly.
No ICMP errors
Routers may return nothing, so traceroute and ping give no useful signal.
Investigation starts in the wrong place
Teams examine firewalls, NSGs, and application settings before route capacity.
The three ingredients behind the failure
Route-prefix processing · Internal IP-block fragmentation · Hardware forwarding-table capacity
Notes: Silent packet death is the umbrella term for several distinct failures in this deck: address conflicts, SNAT exhaustion, and route-table exhaustion. All three drop traffic without a clear error.

## Slide 4
AGENDA
Six areas where AVS networking differs
1
Address planning
The mandatory /22, contiguity, and the ranges you cannot use.
2
HCX and firewall ports
Which ports carry migration traffic and why two transports are needed.
3
Internet egress
Generation 1 managed SNAT versus Generation 2 customer-managed egress.
4
Hybrid connectivity
Interconnect, Virtual WAN scale units, and routing preference.
5
NSX-T, DHCP, and DNS
Tier-0 and Tier-1 behavior, broadcast suppression, and hybrid resolution.
6
Route capacity limits
Prefix ceilings, /28 fragmentation, and the Monday-morning outage.
Notes: Order matters: the early sections build the vocabulary needed for the route-capacity discussion at the end.

## Slide 5
FOUNDATIONAL PLANNING
AVS requires a contiguous /22
/22
1,024 IP addresses
Minimum management address block, reserved before a single workload is placed.
Why it feels excessive
An initial deployment may contain only three ESXi hosts.
Traditional data-center designs might use a /27 for storage and a /28 for a small vMotion network.
By comparison, a /22 looks like an order of magnitude more space than the hardware needs.
Why it is correct
The deployment is an entire software-defined data center, not a handful of isolated hosts.
Azure must add hosts, replace failed hardware, evacuate workloads, patch ESXi, and expand clusters without readdressing the management plane.
The /22 protects the environment from future IP exhaustion.
Notes: The trade-off is real: enterprises have to locate a large, unused, contiguous range. That search should start at the beginning of the engagement, not during deployment.

## Slide 6
FOUNDATIONAL PLANNING
Azure carves the block for you
Azure Resource Manager automatically divides the /22 into predefined infrastructure networks. Customers do not control these sizes.
/26
vCenter and NSX Manager
64 addresses
/25
vMotion
128 addresses
/25
ESXi management
128 addresses
Remainder
Platform lifecycle and growth
Reserved by Azure
Deterministic by design
Automation, predictable lifecycle management, host replacement, and cluster expansion all depend on fixed internal subnets.
Day-zero decision
The management CIDR cannot be treated like a normal workload subnet. Overlap must be identified before deployment.
Expensive to correct
Fixing an addressing mistake later may require rebuilding the private cloud.
Notes: The exact subnet layout can vary by deployment, but the principle holds: the customer supplies one contiguous block and Azure controls everything inside it.

## Slide 7
RESTRICTED ADDRESS SPACE
Ranges you cannot bring into AVS
AVS uses RFC 1918 private addressing, but not every private range is safe. Several conflict with Azure or NSX-T internal infrastructure.
PROHIBITED
172.17.0.0/16
Used by Docker networking
Used by Azure internal containerized management services
Used by hardware telemetry and health-management components
NSX-T INTERNAL
169.254.0.0/24
169.254.2.0/23
Reserved for NSX-T internal overlay functions
Supports peering and transit between Tier-0 and Tier-1 gateways
Carries distributed logical routing traffic
NSX-T INTERNAL
100.64.0.0/16
Reserved for internal transit communication
Overlapping advertisements can poison internal NSX routing
Can break BGP peering with the Azure underlay
What happens when you ignore this:
The managed underlay takes precedence, the hypervisor cannot tell workload traffic from internal Azure management traffic, and workload packets disappear inside the virtual switching layer. Symptoms are TCP retransmissions and application timeouts with no ICMP unreachable response.
Notes: Address exclusions are not arbitrary. They protect infrastructure services that are invisible to the VMware tenant. Validate the enterprise address plan against these ranges before deployment.

## Slide 8
HCX AND FIREWALL DESIGN
The ports that carry migration traffic
TCP 443
Management access
vCenter and management plane access.
TCP 8000
vMotion
Carries live migration of active workloads.
UDP 4500
IPsec / IKEv2
Encapsulates the HCX transport tunnel.
TCP + UDP 5201
Diagnostics
Service-mesh diagnostics and throughput testing.
The live-migration problem these ports exist to solve
A live migration must transfer virtual disks, active memory, and memory pages that keep changing during the move.
High-write workloads such as SQL Server continually dirty memory pages.
The migration must transfer memory changes faster than the workload generates them, or it never converges.
Notes: Port 5201 is worth calling out on assessments. Validating throughput before the first live migration prevents a failed cutover window.

## Slide 9
HCX AND FIREWALL DESIGN
Why HCX needs two different transports
TCP 8000
Reliable migration state
TCP provides reliable delivery for vMotion.
Missing memory data could destabilize or crash the guest operating system.
TCP maintains the migration's state machine.
Weakness: reduced throughput over high-latency WAN links because of acknowledgments, windowing, and retransmission behavior.
UDP 4500
High-throughput WAN transport
HCX carries an IPsec tunnel over UDP 4500.
UDP avoids standard TCP acknowledgment delays.
HCX applies its own compression, deduplication, error handling, and WAN optimization inside the tunnel.
Result: reliable migration-state handling and high-throughput transport are separated rather than compromised.
Notes: This split is the reason both ports must be open end to end. Blocking UDP 4500 does not stop migration outright; it degrades it until large workloads stop converging.

## Slide 10
EXPRESSROUTE
Four-byte BGP ASNs are not optional
An ASN identifies a routing domain in BGP. Traditional implementations used 16-bit, two-byte ASNs.
Azure's software-defined network uses 32-bit, four-byte ASNs.
AVS ExpressRoute connectivity requires native four-byte ASN support throughout the routing path.
AS_TRANS 23456
Older routers that understand only two-byte ASNs may substitute this placeholder. Basic BGP communication survives, but the real routing path is obscured.
Unreliable path selection
Route-path decisions can no longer be trusted.
Weakened loop prevention
BGP's protection against routing loops is undermined.
Indistinguishable circuits
Multiple ExpressRoute circuits and transit paths become hard to tell apart.
Deployment halt
AVS may reject or stop the deployment if four-byte ASNs are not properly supported.
Operational implication
Legacy routing hardware may require upgrade or replacement.
AVS readiness assessments must include router ASN capability.
Cloud adoption exposes hidden dependencies on aging on-premises equipment.
Notes: This is a common late surprise. Adding ASN capability to the readiness checklist costs nothing and avoids a blocked deployment.

## Slide 11
INTERNET EGRESS · GENERATION 1
The managed SNAT model
Generation 1 offered a Microsoft-managed source NAT service, enabled through Azure.
Private workload addresses were translated to Microsoft-managed public IP addresses.
It supported internet software updates, external API access, and basic outbound connectivity.
What made it attractive
Simple to enable
Fast deployment
No customer-managed firewall required
Minimal initial network design
HARD CEILING
128,000
concurrent connections
The number looks large until you count what a modern estate actually opens:
SaaS platforms
Telemetry endpoints
Certificate-revocation services
APIs and update services
Notes: Hundreds of VMs collectively create a very large number of simultaneous NAT translations. The ceiling is reached faster than most teams expect.

## Slide 12
INTERNET EGRESS · GENERATION 1
How port exhaustion actually presents
1
Connections linger
Closed sessions stay in the translation table during TCP TIME_WAIT, idle timeouts, and HTTP keep-alive intervals.
2
The table fills
Lingering entries keep consuming ports, so the table fills even when applications appear to have closed their sessions.
3
New connections drop
Outbound connections are silently dropped. Applications see delayed responses, random timeouts, and intermittent failures.
4
Diagnosis stalls
Engineers cannot inspect the managed NAT translation table. The service behaves as a black box.
Managed SNAT drops ICMP
Ping and traditional traceroute are unavailable, so the usual first-line diagnostics return nothing useful.
Use TCP-oriented tools instead
TCPing · Nmap · Application-level tests
Notes: Lack of visibility is the real cost of the managed model. Incident response slows because the failing component cannot be inspected.

## Slide 13
INTERNET EGRESS · GENERATION 2
Bring your own egress
Generation 2 removes the managed SNAT model and integrates AVS with a native Azure virtual network. Customers deploy their own egress platform.
Azure Firewall
Palo Alto Networks NVA
Fortinet NVA
Other third-party appliance
Customer-controlled public IPs
Egress addresses belong to the customer, not the platform.
Full visibility
Firewall logs, NAT translations, connection state, and security events are all inspectable.
Centralized policy
Egress policy is enforced in the same place as the rest of the Azure estate.
Real troubleshooting
A measurable improvement over the Generation 1 black-box service.
Notes: The trade is control for responsibility. Everything the platform used to handle silently now belongs to the customer's design.

## Slide 14
INTERNET EGRESS · GENERATION 2
The route that makes the design work
AVS workloads
NSX-T Tier-0
avs-nsx-gw
avs-nsx-gw-1
Firewall or NVA
Internet
The configuration
A user-defined route directs 0.0.0.0/0 to the firewall's private IP address.
The route table must be associated with the Generation 2 subnets avs-nsx-gw and avs-nsx-gw-1.
These are the AVS-specific NSX gateway uplink subnets in the virtual network associated with the private cloud.
Why at the transit layer
These subnets are the injection point between Azure's software-defined routers and the NSX-T Tier-0 layer. Applying the UDR there forces internet-bound traffic into the inspection path rather than relying on dynamically learned default routes.
What it prevents
A BGP-learned default route can send outbound traffic through Azure Firewall while return traffic arrives via ExpressRoute. A stateful firewall drops return traffic it never saw open. The targeted UDR keeps the path symmetric.
Notes: Asymmetric routing is one of the most common Generation 2 design faults. It usually appears as intermittent connection resets rather than a clean failure.

## Slide 15
HYBRID CONNECTIVITY
Connecting multiple private clouds
Generation 1 · AVS Interconnect
AVS Interconnect linked multiple private clouds and was explicitly non-transitive.
If Cloud A connects to Cloud B, and Cloud B connects to Cloud C, then A cannot reach C through B.
Architects used to hub-and-spoke transit often see this as a limitation requiring direct or full-mesh connections.
Why non-transitive is deliberate
Interconnect traffic runs over dedicated ExpressRoute infrastructure. Letting one cloud act as a transit hub would force its edge devices to carry unrelated traffic, creating a noisy-neighbor condition. Non-transitivity protects performance isolation, failure-domain boundaries, and latency predictability.
Generation 2 · Native Azure networking
Generation 2 moves toward native Azure networking constructs.
Azure VNet peering uses Microsoft's software-defined backbone.
ExpressRoute Global Reach connects circuits across Microsoft's global network.
Both reduce reliance on AVS-specific interconnect constructs.
Design consequence
Inter-region connectivity becomes an ordinary Azure networking decision rather than an AVS-specific one.
Notes: When clients push back on non-transitivity, the isolation argument usually lands: they are protected from another private cloud's bulk transfer consuming their edge capacity.

## Slide 16
HYBRID CONNECTIVITY
Virtual WAN scale units and branch traffic
500 Mbps
per site-to-site VPN gateway scale unit
Two gateway instances are deployed for redundancy. Their capacity should not be added together when sizing supported aggregate throughput.
Capacity planning
Add the aggregate throughput of all branches.
Account for packet rate and encryption overhead.
Provision for peak, not average, conditions.
Bandwidth totals alone are not enough
VPN gateways perform IPsec encryption and decryption, which consumes CPU.
Required operations include IKEv2, ESP processing, and AES-256 encryption.
A large number of tunnels and packets can exhaust gateway compute even when nominal bandwidth looks sufficient.
What under-provisioning looks like
Gateway CPU reaches 100%
Packets are queued in memory.
Queuing introduces jitter
Voice, real-time apps, and synchronous replication degrade.
Buffers exhaust
Packets are dropped outright.
TCP reacts
Window sizes shrink and branch performance collapses.
Notes: Cost savings from under-provisioning gateways rarely stay contained. They surface as branch-wide performance complaints that are hard to attribute.

## Slide 17
ROUTING PREFERENCE
Hot potato or cold potato
Azure lets you choose between ISP network routing and Microsoft network routing. The choice is a cost and predictability trade-off.
Hot potato
ISP network routing
Microsoft hands traffic to the public internet as soon as possible. Traffic from an AVS environment in Virginia reaches a nearby peering point, then crosses public transit providers to the destination.
BENEFITS
Lower Azure egress cost
TRADE-OFFS
Route changes · Unpredictable latency · Variable jitter · Dependence on multiple public ISPs
Cold potato
Microsoft network routing
Microsoft keeps traffic on its own network as long as possible. It crosses Microsoft's private global backbone and is handed to a local ISP near the destination.
BENEFITS
Stable latency
Lower jitter
Reduced public-internet exposure
TRADE-OFFS
Higher egress cost
Notes: Base the selection on workload requirements rather than default preference. Latency-sensitive applications frequently justify Microsoft network routing despite the cost difference.

## Slide 18
NSX-T
Internal routing architecture
AVS workload networks are implemented as NSX-T segments, with logical routing provided by Tier-0 and Tier-1 gateways.
Tier-1 gateway
EAST-WEST TRAFFIC
Moves traffic between internal workload segments.
Operates in active-standby high availability.
Traffic may be processed by distributed logical routing close to the workloads.
Internal communication can stay inside the AVS environment.
Tier-0 gateway
NORTH-SOUTH TRAFFIC
Connects workloads to Azure, on-premises networks, and the internet.
Operates in active-active mode.
Processes BGP routes, NAT, firewall policy, and external traffic.
Equal-Cost Multipath
FLOW DISTRIBUTION
Tier-0 uses ECMP to distribute traffic across gateways.
A deterministic hash over source IP, destination IP, source port, and destination port selects the path.
All packets in a flow stay on one path; different flows spread across Tier-0 nodes.
This prevents out-of-order delivery and increases aggregate throughput.
Notes: The tram analogy works well here: Tier-1 moves people between terminals, Tier-0 is the road out of the airport.

## Slide 19
HCX LAYER-2 STRETCH
The DHCP broadcast trap
Layer-2 stretching lets migrated VMs keep their IP addresses, original subnet, and original default gateway, which supports migration without immediate readdressing. It also introduces a failure that looks like a broken network.
1
VM requests an address
A newly created VM on the Azure side sends a DHCP Discover broadcast.
2
NSX-T blocks the broadcast
DHCP broadcasts do not cross the HCX Layer-2 extension by default.
3
No offer arrives
The VM never receives a DHCP offer.
4
It reads as a network failure
The symptom points at DHCP or connectivity rather than at a deliberate policy.
Why NSX-T suppresses it
A WAN link is not a local Ethernet switch. Broadcast traffic must be replicated across the overlay, and unrestricted broadcasts can create encapsulation overhead, WAN saturation, VPN gateway CPU exhaustion, and broadcast storms.
The supported workaround
While stretched, disable the DHCP filtering options in the NSX segment-security profile so requests reach the on-premises DHCP server.
Do not configure NSX DHCP relay while the network is stretched; clients can receive incorrect or no responses.
After gateway failover or removal of the extension, configure NSX DHCP relay or an NSX DHCP server.
Notes: This one costs migration teams hours. Add it to the runbook rather than leaving it to be rediscovered per engagement.

## Slide 20
HYBRID DNS
Resolving AVS names from on-premises
168.63.129.16
The Azure platform DNS address
An Anycast virtual address, not a normal internet-routed DNS server. Traffic to it is intercepted locally by the Azure platform and forwarded into Azure's internal DNS fabric.
The hybrid gap
On-premises users need to resolve private AVS names.
Those records are not published in public DNS.
Traditional on-premises DNS servers cannot reach Azure platform DNS directly.
Azure DNS Private Resolver
Deploy the resolver in an Azure VNet with an inbound endpoint subnet and an outbound endpoint subnet. Small /28 subnets are sufficient. The inbound endpoint receives a private IP that on-premises DNS forwards to.
1
On-premises client
2
On-premises DNS server (conditional forwarder)
3
VPN or ExpressRoute
4
Private Resolver inbound endpoint
5
Azure platform DNS
The response returns through the same path, providing private hybrid resolution without standalone DNS servers in Azure.
Notes: Conditional forwarding for the AVS namespace is the whole integration. It avoids deploying and maintaining DNS VMs in Azure purely for hybrid resolution.

## Slide 21
ROUTE CAPACITY
The limits nobody sees until they are hit
~1,000
route prefixes
Azure VNet limit
~1,024
prefixes
NSX-T Tier-0 gateway virtual NIC limit
/28
fragmentation unit
Advertised space is fractured into 16-address blocks
Why hardware sets the ceiling
Azure uses SmartNICs with programmable hardware such as FPGAs to process routes, ACLs, encapsulation, and security functions without the host CPU.
Routes are stored in ternary content-addressable memory (TCAM), which is fast but physically limited and expensive.
The routing fabric must standardize how address blocks consume hardware entries.
The arithmetic of /28 fragmentation
One /24
256 addresses
16 prefix slots
One /22
1,024 addresses
64 prefix slots
The AVS management network consumes route capacity before a single workload network is added.
Notes: Internal route capacity varies with host count, so a three-node cluster supports fewer /28 chunks than a larger one. Adding hosts does not remove the VNet-level ceiling, which is a separate hard constraint.

## Slide 22
ROUTE CAPACITY
How 800 migrated VMs become 800 routes
The problem MON solves
A VM moved across a stretched Layer-2 network keeps its on-premises default gateway. Traffic travels from Azure back to on-premises, through the original gateway, and back toward Azure. This is tromboning, or hairpinning.
What Mobility Optimized Networking does
The VM keeps its original IP address.
HCX injects a /32 host route for the migrated VM.
The /32 tells Azure the individual VM is now local to AVS.
Traffic no longer returns through the on-premises gateway.
THE PREFIX BUDGET
Prefix limit
~1,000
Consumed by 800 migrated VMs
800
Remaining for everything else
~200
That remaining capacity must still cover:
Management routes · VPN routes · DNS routes · Workload subnets · Other hybrid connectivity routes
Notes: Every migrated VM receives its own /32 and each /32 counts as one prefix. Migration batch sizing has to be driven by this number, not by storage or compute throughput.

## Slide 23
ROUTE CAPACITY
What happens at prefix 1,001
The Azure forwarding table stops accepting routes
Newly migrated VMs will:
Power on normally.
Appear fully operational in vCenter.
Lack a functional underlay route.
Fail to communicate, with no clear signal from monitoring.
Where teams look first
Firewall rules
Network security groups
Application services
Guest operating systems
The actual problem
Exhausted hardware route capacity.
Nothing in the guest, the firewall, or the application is at fault.
Notes: This is the Monday-morning outage from the opening slide. It is the reason route-prefix consumption belongs on the migration dashboard alongside VM counts.

## Slide 24
REMEDIATION
Route summarization and gateway cutover
1
Move the gateway
Relocate the subnet gateway into Azure so the workload subnet becomes fully local to AVS.
2
Unstretch the network
Remove the Layer-2 extension once the gateway has moved.
3
Withdraw the /32s
NSX-T replaces hundreds of individual host routes with one aggregate prefix.
4
Advertise the summary
A single summarized /24 replaces the host routes and reclaims route-table capacity.
~30
seconds of potential downtime
Route withdrawal is not instantaneous. Updates propagate through NSX Tier-0 gateways, Azure routing components, ExpressRoute, and other BGP peers.
What a 30-second interruption touches
SQL connections
Application connection pools
Stateful firewall sessions
Replication
Cluster heartbeats
Manual restarts often required
Notes: During convergence some devices hold inconsistent forwarding information. Treat the interruption as a planned event with a maintenance window rather than something to be avoided.

## Slide 25
OPERATING MODEL
Migration discipline that prevents the outage
1
Migrate workloads in controlled batches sized against route-prefix capacity.
2
Monitor route-prefix consumption throughout the migration, not just at the end.
3
Schedule gateway cutovers inside maintenance windows.
4
Accept the convergence interruption as a planned event and communicate it to application teams.
5
Verify the summarized route is active and the /32 routes have been withdrawn.
6
Confirm prefix consumption has returned to baseline before starting the next batch.
Networking and project management are inseparable in AVS. Batch size depends on prefix capacity, cutover timing depends on BGP convergence, and network architects need to be in migration planning from the beginning.
Notes: This slide is the practical takeaway for delivery teams. If nothing else survives the session, this checklist should.

## Slide 26
ARCHITECTURAL LESSONS
What AVS actually asks of you
AVS is not simple VMware hosting
It is an integration of VMware management tools, NSX-T networking, ExpressRoute, Azure VNets, and Azure's physical fabric. Traditional data-center practice cannot be transferred without modification.
Hidden limits matter
IP-block exclusions cause black holes. Managed SNAT tables exhaust. VPN gateways are constrained by encryption CPU. Hardware route tables fill. Broadcast suppression breaks DHCP. BGP convergence interrupts applications.
Visibility comes with responsibility
Generation 1 prioritized simplicity but concealed internal state. Generation 2 gives firewall visibility, routing control, and native Azure integration, and hands back UDR design, symmetric routing, capacity management, and summarization.
Notes: Frame Generation 2 honestly with clients: more control is a benefit only if the team is resourced to exercise it.

## Slide 27
IN CLOSING
Cloud networking is not the virtualization of physical cables.
It is an interaction between software engineering, distributed control planes, hardware memory, routing mathematics, and operational procedure. Successful AVS architecture requires strict design discipline and continuous capacity monitoring.
A question worth carrying forward
If AI-driven control planes eventually summarize routes, resize boundaries, and optimize prefix usage in real time, will network architects still count IP addresses, plan route-table capacity, and manage summarization by hand? And if the limits become invisible, who notices when they are reached?
Notes: Close by inviting the room's own experience: which of these limits have they already hit, and what did the symptom look like before they identified the cause?